## Slide 1
SIMATS ENGINEERING
ASSESSMENT TOOL 2
COURSE NAME:
CSA07 COURSE CODE: Computer Networks
COURSE OUTCOME COVERED
CO1: Apply the functions of OSI layer in enabling reliable data transmission across
networks. (BL2, BL3)
Assessment Tool Weightage: 30%
Annexure A
CONCEPT MAPPING
Code of Conduct:
I paluchuri karthik (192525238) (Name / Reg No) certify that this submission is my original work and that
I have adhered to the guidelines specified for this assessment.
I understand that any violation of academic integrity rules will result in disciplinary action.
Signature of the student: paluchuri karthik (192525238)

## Slide 2
Annexure A
CONCEPT MAPPING
1. A partially completed concept map is given below:
Application → Presentation → ______ → Transport → Network → ______ → Physical.
Analyze the missing layers and explain how their functions are essential for reliable
communication.
2. Construct a concept map linking data units (Segment, Packet, Frame, Bits) with their
respective OSI layers and analyze how transformation of data units supports
transmission.
3.Given the concept map:
DataLink→MACAddress→LocalDelivery
Network → IP Address → Global Delivery
Explain how these relationships ensure complete data delivery across networks.
4. A concept map shows:
ErrorControl
→DataLinkLayer→ErrorDetection
→ Transport Layer → Error Correction
Analyze how the interaction between these layers improves reliability in data
transmission.
5. Develop a concept map for web browsing using OSI layers and analyze how failure
in one layer affects the entire communication process.
6. A network issue is represented in the concept map:
Physical ✔ → Data Link ✔ → Network ✖ → Transport ✖ → Application ✖
Analyze the problem and explain how the concept map helps in troubleshooting.

## Slide 3
Question 1: Missing OSI Layers and Their Functions
Completed Concept Map
Application \(\rightarrow \) Presentation \(\rightarrow \) Session \(\rightarrow \) Transport
\(\rightarrow \) Network \(\rightarrow \) Data Link \(\rightarrow \) Physical.
Functional Analysis
•
Session Layer:
o Establishes, manages, and terminates communication sessions between local and
remote applications.
o
Handles authentication, authorization, and session restoration (checkpointing) so a
connection can resume from its last known good state if interrupted.
•
Data Link Layer:
o Provides reliable node-to-node data transfer across a physical link.
o Packages raw bits from the Physical layer into structured frames.
o Implements physical addressing (MAC addresses), flow control, and error
detection to ensure local data delivery is accurate.
Question 2: Data Units and OSI Layers Mapping
Concept Map
•
•
•
•
Transport Layer \(\rightarrow \) Segment (or Datagram for UDP)
Network Layer \(\rightarrow \) Packet
Data Link Layer \(\rightarrow \) Frame
Physical Layer \(\rightarrow \) Bits
Transformation Analysis (Encapsulation and Decapsulation)
•
Downstream (Encapsulation): Data moves down the stack, and each layer adds
structural control data (headers/trailers). The Transport layer splits data into manageable
segments. The Network layer adds IP addresses to form packets for routing. The Data
Link layer wraps packets into frames with physical MAC addresses. The Physical layer
converts frames into electrical or optical bits for medium transmission.
•
Upstream (Decapsulation): The receiving device strips away these headers step-by-step
to process and verify the data. This structured transformation abstracts complex
networking tasks, letting each layer focus purely on its specific operational job.
Question 3: Addressing and Delivery Systems

## Slide 4
Analysis of Relationships
•
Data Link Layer \(\rightarrow \) MAC Address \(\rightarrow \) Local Delivery: This
relationship operates within a single local network segment (LAN). Devices use
hardware-burned MAC addresses to forward data frames directly between adjacent nodes
on the same physical link.
Network Layer \(\rightarrow \) IP Address \(\rightarrow \) Global Delivery: This
relationship spans across multiple interconnected networks. Logical IP addresses allow
routers to determine the best path across different subnets, moving packets from the
original source network to the final destination network.
•
Ensuring Complete Delivery: Local delivery alone cannot cross a router, and global
delivery alone does not know which specific machine on a local switch should receive the
data. Together, IP routing gets the data to the correct neighborhood, and MAC addressing
delivers it to the correct house.
Question 4: Error Control Interaction Across Layers
Interaction Analysis
•
Data Link Layer (Error Detection): This layer handles immediate, hop-by-hop
integrity checks. It utilizes mathematical checks like Cyclic Redundancy Check (CRC) in
the frame trailer to identify if bits were corrupted over the physical wire. If a frame is
broken, it is typically discarded right away.
•
Transport Layer (Error Correction): This layer provides end-to-end reliability. It uses
sequence numbers and acknowledgments (like TCP ACKs). If the receiving end notices a
missing segment (potentially dropped by the Data Link layer below), it requests a
retransmission from the original source.
•
Reliability Improvement: This split responsibility saves network bandwidth. Catching
errors early at the Data Link layer prevents corrupted data from traveling further up the
stack, while the Transport layer guarantees that any dropped data is successfully
recovered.
Question 5: Web Browsing Concept Map and Failure Analysis
Web Browsing OSI Concept Map
•
Application / Presentation / Session Layers: HTTP/HTTPS protocols structure web
requests; TLS/SSL handles encryption.
•
Transport Layer: TCP establishes a reliable connection via a 3-way handshake to
destination port 80 or 443.

## Slide 5
•
Network Layer: IP routes the web traffic across the internet using source and destination
IP addresses.
•
Data Link / Physical Layers: Ethernet or Wi-Fi transmits the web data as physical
signals over local hardware.
Failure Cascading Analysis
•
The Impact: If a lower layer fails (e.g., a broken Network Layer due to a lost IP route),
the entire upper communication chain collapses.
Why it happens: Layers are strictly dependent on the services provided by the layers
directly beneath them. If the Network layer cannot route packets, the Transport layer
cannot maintain its TCP connection, preventing the Application layer from loading the
website. The user sees a "Network Timeout" or "No Internet" error.
Question 6: Troubleshooting via Concept Map
Problem Analysis
•
Physical (\(\checkmark \)) and Data Link (\(\checkmark \)): Local hardware, cables,
Wi-Fi connections, and local switch communications are functioning perfectly.
•
Network (\(\mathbf{X}\)): The communication failure originates right here at the
Network layer.
•
Transport (\(\mathbf{X}\)) and Application (\(\mathbf{X}\)): These layers fail as a
direct consequence of the Network layer failure.
How the Concept Map Helps in Troubleshooting
•
Isolates the Fault: The map tells a technician to completely skip troubleshooting cables,
network cards, or software applications.
Targets the Root Cause: It pinpoints the investigation directly to Network layer issues.
A technician should immediately check for misconfigured static IP addresses, dead
default gateways, subnets mismatches, or faulty router tables.

## Slide 6
Criteria | Weightage (%) | Level 4 (Exemplary) | Level 3 (Proficient) | Level 2 (Developing) | Level 1 (Beginning)
Concept Identification | 20% | Accurately identifies all relevant OSI layers, concepts, and relationships | Identifies most concepts with minor omissions | Identifies limited concepts; some inaccuracies | Unable to identify key concepts correctly
Concept Mapping Structure | 25% | Constructs a clear, logical, and well- organized concept map with proper hierarchy and connections | Concept map is mostly clear with minor structural issues | Concept map lacks clarity, organization, or proper flow | No clear structure or incorrect mapping
Linking & Relationships | 20% | Clearly establishes correct relationships between layers, functions, and processes | Relationships are mostly correct with minor errors | Limited or partially correct relationships | Incorrect or missing relationships
Application & Analysis | 20% | Effectively applies concepts to explain processes (e.g., encapsulation, error control) with strong reasoning | The application is correct but lacks depth in analysis | Basic application with weak explanation | Unable to apply concepts correctly
Explanation & Clarity | 15% | Provides a clear, concise, and well- structured explanation supporting the concept map | Explanation is understandable with minor gaps | Explanation is unclear or incomplete | No clear or meaningful explanation
RUBRICS FOR CALCULATION